## Slide 1
Technical Slide Deck

## Slide 2: Presentation Overview
Design Objectives / Technical Roadmap & Vision
OCORA Scope
CCS On-Board Logical Architecture
CCS On-Board Physical Architecture
Building Blocks
Train Integration Scenarios
Network Topology Scenarios
Computing Platform
Functional Vehicle Adapter (FVA)
Modular Safety
Methodology & Tooling
Operational Concept

## Slide 3: Design Objectives Technical Roadmap & Vision

## Slide 4: OCORA Design Objectives
Modular
RAMSS
Exchangeable
Migratable
Portable
Evolvable
Secure
A reasonable number of Building Blocks are defined for CCS On-Board.
Each Building Blocks has standardised functionality, standardised interfaces, standardised performance (RAM), standardised safety (including Tolerable Functional Failure Rate [TFFR], Safety Integrity Level [SIL] and Safety Related Application Conditions [SRAC]), and standardised security.
Ability to replace CCS On-Board Building Block. In the context of OCORA exchangeability means the ability to replace one or multiple OCORA defined building blocks with (a) respective building block(s) of (an)other supplier(s), without affecting other building blocks of the train or the overall CCS on-board system.
Ability to introduce changes to any CCS On-Board Building Block. In the context of OCORA migrateability is the ability to introduce changes to one or multiple OCORA defined building blocks, without affecting other building blocks or the overall CCS on-board system.
Ability to easily adapt the CCS On-Board to new technologies and to easily add new Building Blocks. In the context of OCORA evolvability means the ability to easily adopt to new technologies or to extend the functionality of an on-board CCS system without the involvement of the original supplier.
Ability to protect the CCS On-Board from attacks. In context of OCORA security means the protection of (especially safety related communication and data used in) CCS on-board systems against threats (in particular cyber-attacks and hacks). To achieve this, all main security functionality like identify, protect, detect, respond and recover are considered.
Ability to port CCS On-Board Software Building Blocks (software applications) from one computing platform to another. In the context of OCORA portability is achieved when a functional application, based on the generalized abstraction, runs un-changed on different (computing) platform implementations. For this, the functional application shall only use external functions through a defined application programming interface (API).

## Slide 5: Technical Roadmap – Current Situation
Today, the proprietary CCS On-Board System is fully integrated in the proprietary Vehicle Environment, driving costs, risks, and complicating the life-cycle and obsolescence management for the railway undertakings. This current situation hinders the railways to take advantage of innovations in a timely and cost-effective manner.
CCS On-Board Constituent
CCS On-Board Constituent
CCS On-Board Building Block
Train Adapter
CCS On-Board Constituent
Step 0: Current Situation
Radar
IMU
GSM-R
CCS On-Board System
Odometry
Vehicle Environment
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
Odometry
IMU
MCG
Vehicle Network
Public Mobile Radio for
Passenger WiFi Service
GNSS
EURO Balise Reader
EURO Loop Reader

## Slide 6: Technical Roadmap Step 1 – Short-Term
The interface between the proprietary CCS On-Board System and the Vehicle Environment is unambiguously standardised.
CCS On-Board Constituent
CCS On-Board Constituent
CCS On-Board Building Block
CCS On-Board Constituent
Step 1: Short-Term (TSI-2022)
Odometry
Radar
IMU
GSM-R
CCS On-Board System
Odometry
IMU
Public Mobile Radio for
Passenger WiFi Service
Step 1 is simplifying life-cycle and obsolescence management for the CCS On-Board System.
Step 1 is enabling exchangeability, is supporting migrateability and portability of the CCS On-Board System without affecting the Vehicle Environment.
EURO Balise Reader
EURO Loop Reader
Vehicle Environment
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
MCG
Vehicle Network
GNSS
Train Adapter

## Slide 7: Technical Roadmap Step 2 – Mid-Term
The CCS On-Board System consists of a well balanced number of CCS On-Board Building Blocks. Each Building Blocks has standardised functionality, standardised performance (RAM), standardised safety (including Tolerable Functional Failure Rate [TFFR], Safety Integrity Level [SIL] and Safety Related Application Conditions [SRAC]), standardised security, and standardised interfaces towards other building blocks and/or external systems, allowing to mix-and-match Building Blocks from different suppliers.
The CCS On-Board Building Blocks communicate with each other, with the Vehicle Subsystems and any Off-Board System via the standardized CCS Communication Network (CCN) and the Connectivity Services, using FRMCS or the MCG. Cyber Security Services provide Identity and Access Management (IAM), security patch updates, synchronized time services, and other means to allow secure operations.
CCS On-Board Building Block
CCS On-Board Building Block
CCS On-Board Building Block
CCS On-Board Building Block
CCS On-Board Building Block
CCS On-Board Building Block
Step 2: Mid-Term (TSI-2025)
Connectivity
Services
Perception
GNSS
Odometry
Radar
IMU
GSM-R
FRMCS
MCG
Odometry
Public Mobile Radio for
Passenger WiFi Service
CCN
CCN
CCS Off-Board Support
Remote Maintenance
Asset Management
Remote Supervision
Remote Driving
Step 2 is enabling the sharing of the following peripheral devices between CCS On-Board and the Vehicle Environment:
Mobile Communication Gateway (MCG)
GNSS antenna and receiver
Inertial Measurement Unit (IMU)
Step 2 is enabling exchangeability, is supporting migrateability and portability of the individual CCS On-Board Building Blocks without affecting other CCS On-Board Building Blocks, the Vehicle Environment, and any Off-Board Systems. This step is simplifying life-cycle management and is the basis for the railways to consider adding new functionality such as:
Remote Maintenance
Asset Management
Absolut continues safe localisation (GNSS)
Safe Train Integrity determination
Safe Train Length determination
ETCS L3
ATO GoA 1-4
Remote Supervision
Remote Driving
EURO Balise Reader
EURO Loop Reader
Vehicle Environment
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
Vehicle Network
Com Net
Sec Net
Cyber Security
Services
CCS On-Board System
Train Adapter

## Slide 8: Technical Roadmap Step 3 – Long-Term
The CCS On-Board System includes a safe computing platform, hosting CCS Building Blocks as applications that communicate with each other, with the Vehicle Subsystems and any Off-Board System via a standardized API, the standardized CCS Communication Network (CCN) and the Connectivity Services, using FRMCS or Public Mobile Radio.
Due to the increased performance of the CCS On-Board localisation, EURO Balise and EURO Loop readers may not be needed anymore for trains running on certain tracks.
CCS On-Board Building Block
CCS On-Board Building Block
Application 1
Application 2
Application 4
Application 3
Safe Computing Platform
Step 3: Long-Term (TSI-2028)
Perception
GNSS
Odometry
Radar
IMU
FRMCS
MCG
Odometry
CCN
CCN
Public Mobile Radio for
Passenger WiFi Service
EURO Balise Reader (Option)
EURO Loop Reader (Option)
Step 3 is simplifying the development and deployment of new functionalities by separating the business logic from the hardware. In addition, the Safe Computing Platform is reducing the number of CCS computing units (CCUs) needed, increasing availability and reducing maintenance efforts.
Step 3 is simplifying the portability of the business logic.
Vehicle Environment
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
Vehicle Network
Com Net
Sec Net
Cyber Security
Services
Connectivity
Services
Train Adapter
CCS Off-Board Support
Remote Maintenance
Asset Management
Remote Supervision
Remote Driving
CCS On-Board System

## Slide 9: Technical Roadmap Step 4 – Vision
The standardised CCS On-Board Communication Network (CCN) is fully integrated with the Vehicle Network, allowing to interface from any CCS On-Board Application directly with any Vehicle Subsystems and vice-versa. The need for a Train Adapter vanishes and certain Applications from the Vehicle Environment may be hosted on the CCS On-Board Safe Computing Platform.
Due to the increased performance of the CCS On-Board localisation through better sensor fusion algorithms, the use of GNSS localisation, digital map data, and augmentation data, the EURO Balise and EURO Loop readers are not needed anymore.
Step 4: Vision ( > TSI 2028)
CCS On-Board Building Block
CCS On-Board Building Block
Connectivity
Services
Perception
GNSS
Odometry
Radar
IMU
FRMCS
Application 1
Application 2
Application 4
Application 3
Safe Computing Platform
CCN
MCG
Odometry
CCN
Public Mobile Radio for
Passenger WiFi Service
Step 4: eliminating the EURO Balise and EURO Loop readers further reduces the maintenance efforts and enables the infrastructure managers to implement changes more quickly.
Step 4: integrating the CCS On-Board domain with the Vehicle Environment allows to reuse peripherals and applications throughout the whole train, reducing the level of hardware systems and applications needed on a train. This again will increase availability and will reduce maintenance
Vehicle Environment
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
TCMS Subsystem
TCMS Subsystem
Operator Subsystem
Vehicle Network
Cyber Security
Services
Com Net
Sec Net
CCS Off-Board Support
Remote Maintenance
Asset Management
Remote Supervision
Remote Driving
CCS On-Board System

## Slide 10: OCORA Scope

## Slide 11: OCORA Scope – Logical Architecture
1)
May be moved into the PTU-OS / LOC&PAS domain.
SS-nnn Respective subset contains information for the interface
SS-nnn* Respective subset does not address the interface but should contain the information in the future.
CCS On-Board (CCS-OB)
Train Adapter (TA)
CCS Off-Board Support (COBS)
(Cyber)-Security (CSEC)

## Slide 12: OCORA Scope – Physical Architecture (Legacy Train)
CCS On-Board (CCS-OB)
(Cyber)-Security (CSEC)
Train Adapter (TA)
CCS Off-Board Support (COBS)
Connectivity Services

## Slide 13: OCORA Scope – Physical Architecture (New Generation Trains)
CCS On-Board (CCS-OB)
CCS Off-Board Support (COBS)
Connectivity Services
(Cyber)-Security (CSEC)

## Slide 14: CCS On-Board (CCS-OB) Logical Architecture

## Slide 15: Logical Architecture CCS-OB Actors, External Interfaces, Functional Components
1)
1) May be moved into the PTU-OS / LOC&PAS domain.
CCS On-Board (CCS-OB)
May be moved into the PTU-OS / LOC&PAS domain.
SS-nnn Respective subset contains information for the interface
SS-nnn* Respective subset does not address the interface but should contain the information in the future.

## Slide 16: Logical Architecture CCS-OB Functional Clustering for Building Block Assignment
*
Current CCS-OB Functionality
Future CCS-OB Functionality
European Train Protection On-Board
(ETP-OB)
National Train Protections
(NTPs)
Train Display System
(TDS)
Perception
On-Board
(PER-OB)
Signal Converter
(SCV)
Automatic Train Operation
On-Board
(ATO-OB)
Monitoring, Diagnostic, Configuration, Maintenance
On-Board
(MDCM-OB)
Remote Manual Train Operation
On-Board
(RMTO-OB)
1)
1) May be moved into the PTU-OS / LOC&PAS domain.
CCS On-Board (CCS-OB)
CCS Off-Board Support (COBS)
Digital Map Repository
On-Board
(DREP-OB)
Driver Advisory System
On-Board
(DAS-OB)
Train Adapter (TA)
(Cyber)-Security (CSEC)
May be moved into the PTU-OS / LOC&PAS domain.
SS-nnn Respective subset contains information for the interface
SS-nnn* Respective subset does not address the interface but should contain the information in the future.
Virtual ETCS Transponder Service
(VETS)
Localisation
On-Board
(LOC-OB)
Cabin Voice Radio
(CVR)
Virtual Train Coupling S.
On-Board
(VTCS-OB)

## Slide 17: Logical Architecture ETP-OB Actors, External Interfaces, Components
1)
1) May be moved into the PTU-OS / LOC&PAS domain.
European Train Protection On-Board (ETP-OB)
May be moved into the PTU-OS / LOC&PAS domain.
SS-nnn Respective subset contains information for the interface
SS-nnn* Respective subset does not address the interface but should contain the information in the future.

## Slide 18: Logical Architecture LOC-OB Actors, External Interfaces, Components
1)
1) May be moved into the PTU-OS / LOC&PAS domain.
Localisation On-Board (LOC-OB)
May be moved into the PTU-OS / LOC&PAS domain.
SS-nnn Respective subset contains information for the interface
SS-nnn* Respective subset does not address the interface but should contain the information in the future.

## Slide 19: Logical Architecture FVA Actors and External Interfaces
1) May be moved into the PTU-OS / LOC&PAS domain.
May be moved into the PTU-OS / LOC&PAS domain.
SS-nnn Respective subset contains information for the interface
SS-nnn* Respective subset does not address the interface but should contain the information in the future.

## Slide 20: CCS On-Board (CCS-OB) Physical Architecture

## Slide 21: Physical Architecture CCS-OB – Legacy Train Actors, Interfaces, Hardware Components
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN (SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN (SS-147)
CCN (SS-147)
CI-NTP
SS-036
SS-044
SS-037
HMI-UIDR
HMI-CVD
HMI-TDS
PI-PER-OB
PI-VLS
PI-CMD
GSM-R Voice
HMI-CVR
SS-035
SS-057
HW-SIL4
CCS On-Board (CCS-OB)
UIC
CCN (SS-147)

## Slide 22: Physical Architecture CCS-OB – NG Train Actors, Interfaces, Hardware Components
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN
(SS-147)
CCN (SS-147)
SS-035
SS-057
HW-SIL4
CCS On-Board (CCS-OB)
CI-NTP
SS-036
SS-044
HMI-UIDR
HMI-CVD
HMI-TDS
PI-PER-OB
PI-VLS
PI-CMD

## Slide 23: Building Blocks

## Slide 24: Building Blocks
A building block is a sourceable unit of the CCS on-board system (hardware and/or software), having standardised functionality, standardised performance (RAM), standardised safety (including Tolerable Functional Failure Rate [TFFR], Safety Integrity Level [SIL] and Safety Related Application Conditions [SRAC]), standardised security and standardised interfaces towards other building blocks and/or external systems.
Combined HW/SW Building blocks exclusively communicating with each other through the CCS Communication Network (CCN) through standardise interfaces.
SW Building blocks, deployed on an instance of the generic Safe Computing Platform, shall communicate with each other through the standardised platform independent Application Programming Interface (API). Communication with computing platform external systems will be realised by the computing platform (integrating with the CCN).
Building blocks are modifiable / adaptable and therefore portable / replaceable, without impacting other building blocks.
Definition

## Slide 25: Scenario 1
Monitoring, Diagnostic, Configuration, Maintenance
On-Board
(MDCM-OB)
Driver Advisory System
On-Board
(DAS-OB)
Automatic Train Operation
On-Board
(ATO-OB)
Digital Map Repository
On-Board
(DREP-OB)
Remote Manual Train Operation
On-Board
(RMTO-OB)
European Train Protection On-Board
(ETP-OB)
Localisation
On-Board
(LOC-OB)
Perception
On-Board
(PER-OB)
Train Display
System (TDS) 1)
National Train Protections
(NTPs)
Cabin Voice Radio
Legacy (CVR-L)
User Identification
& Authentication (UIA)
Cabin Voice Radio VoIP (CVR-V)
CCS Communication Network (CCN)
FRMCS
On-Board
System
MCG (CCS)
On-Board
System
Virtual Train Coupling System On-Board
(VTCS-OB)
Security Network
ECN / ECN
Security
Gateway
COM Network
(Cyber)-Security Services (CSS)
Other
Application
(Signal Conv., Virtual ETCS Transponder Service, etc.)
Current CCS-OB Functionality
Future CCS-OB Functionality
CCS On-Board (CCS-OB)
Train Adapter (TA)
CCS Off-Board Support (COBS)
(Cyber)-Security (CSEC)
Connectivity Services
Building Blocks without Safe Computing Platform (dedicated hardware for each functional cluster)
Legacy Train Example

## Slide 26: Scenario 2
Train Display
System (TDS) 1)
National Train Protections
(NTPs)
CCS Communication Network (CCN)
Security Network
ECN / ECN
Security
Gateway
COM Network
(Cyber)-Security Services (CSS)
SIL4 I/O
Ports
FRMCS
On-Board
System
MCG (CCS)
On-Board
System
Current CCS-OB Functionality
Future CCS-OB Functionality
CCS On-Board (CCS-OB)
CCS Off-Board Support (COBS)
Connectivity Services
(Cyber)-Security (CSEC)
European Train Protection On-Board
(ETP-OB)
Localisation
On-Board
(LOC-OB)
Perception
On-Board
(PER-OB)
Cabin Voice Radio
Legacy (CVR-L)
Functional Vehicle
Adapter
(FVA)
Monitoring, Diagnostic, Configuration, Maintenance
On-Board
(MDCM-OB)
Driver Advisory System
On-Board
(DAS-OB)
Automatic Train Operation
On-Board
(ATO-OB)
Digital Map Repository
On-Board
(DREP-OB)
Remote Manual Train Operation
On-Board
(RMTO-OB)
Virtual Train Coupling System On-Board
(VTCS-OB)
Other
Application
(Signal Conv., Virtual ETCS Transponder Service, etc.)
Building Blocks with Safe Computing Platform for some Applications
Legacy Train Example
Train Adapter (TA)
Safe Computing Platform (SCP)
API
API
API
API
API
API
API
API
User Identification
& Authentication (UIA)
Cabin Voice Radio VoIP (CVR-V)

## Slide 27: Scenario 3
European Train Protection On-Board
(ETP-OB)
Localisation
On-Board
(LOC-OB)
Perception
On-Board
(PER-OB)
Train Display
System (TDS) 1)
National Train Protections
(NTPs)
CCS Communication Network (CCN)
Security Network
ECN / ECN
Security
Gateway
COM Network
(Cyber)-Security Services (CSS)
SIL4 I/O
Ports
Safe Computing Platform (SCP)
Safe Computing Platform (SCP)
API
API
API
FRMCS
On-Board
System
MCG (CCS)
On-Board
System
Current CCS-OB Functionality
Future CCS-OB Functionality
CCS On-Board (CCS-OB)
CCS Off-Board Support (COBS)
Connectivity Services
(Cyber)-Security (CSEC)
Functional Vehicle
Adapter
(FVA)
Monitoring, Diagnostic, Configuration, Maintenance
On-Board
(MDCM-OB)
Driver Advisory System
On-Board
(DAS-OB)
Automatic Train Operation
On-Board
(ATO-OB)
Digital Map Repository
On-Board
(DREP-OB)
Remote Manual Train Operation
On-Board
(RMTO-OB)
Virtual Train Coupling System On-Board
(VTCS-OB)
Other
Application
(Signal Conv., Virtual ETCS Transponder Service, etc.)
API
API
API
API
API
API
API
API
Cabin Voice Radio
Legacy (CVR-L)
Building Blocks with Safe Computing Platform for all Applications
Legacy Train Example
Train Adapter (TA)
User Identification
& Authentication (UIA)
Cabin Voice Radio VoIP (CVR-V)

## Slide 28: Scenario 4
European Train Protection On-Board
(ETP-OB)
Localisation
On-Board
(LOC-OB)
Perception
On-Board
(PER-OB)
Train Display
System (TDS) 1)
National Train Protections
(NTPs)
CCS Communication Network (CCN)
Security Network
ECN / ECN
Security
Gateway
COM Network
Identity and Access Management
(IAM-OB)
Time Service (TS-OB)
SIL4 I/O
Ports
Safe Computing Platform (SCP)
Safe Computing Platform (SCP)
API
API
API
FRMCS
On-Board
System
MCG (CCS)
On-Board
System
Current CCS-OB Functionality
Future CCS-OB Functionality
CCS On-Board (CCS-OB)
CCS Off-Board Support (COBS)
Connectivity Services
(Cyber)-Security (CSEC)
Monitoring, Diagnostic, Configuration, Maintenance
On-Board
(MDCM-OB)
Driver Advisory System
On-Board
(DAS-OB)
Automatic Train Operation
On-Board
(ATO-OB)
Digital Map Repository
On-Board
(DREP-OB)
Remote Manual Train Operation
On-Board
(RMTO-OB)
Virtual Train Coupling System On-Board
(VTCS-OB)
Other
Application
(Signal Conv., Virtual ETCS Transponder Service, etc.)
API
API
API
API
API
API
API
Building Blocks with Safe Computing Platform for all Applications
New Generation Train Example
User Identification
& Authentication (UIA)
Cabin Voice Radio VoIP (CVR-V)

## Slide 29: Train Integration Scenarios

## Slide 30: NG-TCN Train – Scenario A
(CCN as physically separated network from Sec Net, Op Net, NG TCN
and Com Net with support for legacy trackside infrastructure)

## Slide 31: NG-TCN Train – Scenario B
(CCN as logically separated network from NG TCN and physically separated
from Sec Net, Op Net and Com Net with support for legacy trackside infrastructure)

## Slide 32: NG-TCN Train – Scenario C
(Common CCN and TCMS network logically separated from A-TCMS and physically
separated from Sec Net, Op Net and Com Net with support for legacy trackside infrastructure)

## Slide 33: NG-TCN Train – Scenario D
(Common CCN and TCMS network physically separated from A-TCMS, Sec Net,
Op Net and Com Net with support for legacy trackside infrastructure)

## Slide 34
(CCN physically separated from Sec Net and Com Net using the OCORA GW connecting to the TCMS / PIS Networks. Support for legacy trackside infrastructure)
Legacy Train

## Slide 35: Network Topology Scenarios

## Slide 36: Scenario A: CCN as physically separated network

## Slide 37: Scenario B: CCN as logically separated network

## Slide 38: Scenario C: Common critical control network logically separated

## Slide 39: Scenario D: Common critical control network physically separated

## Slide 40: Legacy Train – Integration with OCORA-GW

## Slide 41: Computing Platform

## Slide 42: Computing Platform – High Level Architecture
Functional Application (Business Logic)
System Services
Safety Services
Operating System (if needed)
Virtualisation (if needed)
Computing Node(s)
Board Support Package
Hardware Independence *
Platform Independent API
Comm Stack
IT Security
Hardware
Runtime environment
Computing Platform
implements
uses
* It is to be discussed to which extent hardware independence can or should be enforced

## Slide 43: Computing Platform – Deployment Options
Platform options where applications are programmed against PI API
Approaches depicted in the diagram are non-exhaustive. The industry may propose different state-of-the-art solutions.
Likely option for trackside deployments
Option A:
Hardware without operating system
Option B:
Hardware with operating system
Option C:
Separation kernel / hypervisor based system
Multi-Core Node
Board Support Package
Partition
Safety & System Services
PI API
Functional App. Replica
Multi-Core Node
Board Support Package
Partition
Safety & System Services
PI API
Functional App. Replica
Multi-Core Node
Board Support Package
Partition
Safety & System Services
PI API
Functional App. Replica
Multi-Core Node
Board Support Package
Partition
Safety & System Services
PI API
Functional App. Replica
Operating System
Multi-Core Node
Board Support Package
Partition
Safety & System Services
PI API
Functional App. Replica
Operating System
Multi-Core Node
Board Support Package
Partition
Safety & System Services
PI API
Functional App. Replica
Operating System
Multi-Core Node
Board Support Package
Separation Kernel / Hypervisor
Partition
PI API
Func. App. 1 Replica
Partition
PI API
Func. App. 2 Replica
Partition
Safety & System Services
Multi-Core Node
Board Support Package
Separation Kernel / Hypervisor
Partition
PI API
Func. App. 1 Replica
Partition
PI API
Func. App. 2 Replica
Partition
Safety & System Services
Multi-Core Node
Board Support Package
Separation Kernel / Hypervisor
Partition
PI API
Func. App. 1 Replica
Partition
PI API
Func. App. 2 Replica
Partition
Safety & System Services
Multi-Core Node
Board Support Package
Separation Kernel / Hypervisor
Multi-Core Node
Board Support Package
Separation Kernel / Hypervisor
Multi-Core Node
Board Support Package
Virtualisation
Orchestration
Partition
Safety & System Services
PI API
Func. Appl. 1 Replica
Partition
Safety & System Services
PI API
Func. Appl. 1 Replica
VM / Partition
Safety & System Services
PI API
Func. App. 1 Replica
Partition
Safety & System Services
PI API
Func. App. 2 Replica
Operating System
Partition
Safety & System Services
PI API
Func. App. 2 Replica
Operating System
VM / Partition
Safety & System Services
PI API
Func. App. 2 Replica
Operating System
Option D:
Orchestrated virtualisation
environment
Likely options for onboard deployments

## Slide 44: Functional Vehicle Adapter (FVA)

## Slide 45: OCORA – Functional Vehicle Adapter
Details in Document: OCORA-TWS04-010 – Functional Vehicle Adapter - Introduction
ETCS
ATO

## Slide 46: OCORA – Functional Vehicle Adapter: Extensions
Details in Documents: OCORA-TWS04-013 – Design Guideline
ETCS
ATO

## Slide 47: Modular Safety

## Slide 48: OCORA – Modular Safety
  Modular Safety defines the hierarchy between safety cases from building blocks to specific application(s).
  One of the main goal is to reduce the certification efforts (initial- and re-certification) at all levels without degrading the safety level of the analyses.
  Modular Safety shall also defines the safety elements to allow the homologation of stand-alone building blocks:
    Hazardous events based on TSI CCS SUBSET-088
    TFFR (Tolerable Functional Failure Rate) based on TSI CCS SUBSET-088
    Safety requirements based on OCORA Delta release
    Harmonised and generic set of SRAC

## Slide 49: OCORA – Modular Safety - Stakeholders
The integrator of the CCS/ETCS on-board system shall coordinate the activities of the different suppliers to integrate their sub-systems and ensure that finally, ISA and NoBo certificates of the CCS/ETCS on-board system will be delivered by the assessor
 Contracting entities (Oprators)
 Integrator(s)
 Manufacturers (Building Blocks, Application…)
 Other (ISA/ NoBo, DeBo..)

## Slide 50: OCORA – Modularity & Safety Approval
Case of two independent systems made of building blocks from different suppliers
Each color represents a different supplier
  Each building block is delivered to the ETCS on-board integrator with its own ISA/NoBo certificates
  ETCS on-board integrator realise their "safe integration" as defined in era_1209-063 Clarification Note On Safe Integration (I.e. black boxes)
  Based on ETCS on-board ISA/NoBo certificates, CCS on-board integrator realise the safe integration of the STM (I.e. black boxes)
  CCS and ETCS on-board systems are used by the vehicle integrator to get the train type ISA/NoBo certificates (I.e. integration is eased thanks to the FVA)
  The contracting entity can apply for the different vehicle authorisations required
  A generic and systematic approach defined by OCORA, based on CSM-RA will then help any above stakeholder to handle easier (I.e. less delay and costs than today) the evolutions at any level

## Slide 51: OCORA – Modularity & Integration Tasks
Other Subsystems
CCS Trackside
Other Subsystems
SW validation
SW validation
System level
Build. Block design
Building Blocks Testing
Unified Operation concept
System Integration and Validation
Trace
On-board CCS Subsystem
Design refinement
Vehicle level Integration & Testing
Appl. SW Testing
Onboard CCS subsystem level Integration & Testing
Design refinement
Scope of OCORA
SW implement.
 Integrator (System)
 Integrator (onboard)
Moduar integration from « Blocks » to « complete CCS »
1, 2..: integration steps
 Manufacturers (Building Blocks, Application…)
1
2
3
4
5
System Operated and maintained
In OCORA compliant projects, the integrator is identified as the key player for Safety, Integration and Testing of the on-board CCS system.

## Slide 52: OCORA – Modularity & Integration Tasks
In OCORA compliant projects, the integrator is identified as the key player for Safety, Integration and Testing of the on-board CCS system
 Contracting entities (RU §IM)
 Integrator(s)
 Manufacturers (Building Blocks, Application…)
Modular CCS Stakeholders
 Other (ISA/ NoBo, DeBo..)

## Slide 53: Methodology & Tooling

## Slide 54: OCORA Requirements Engineering
Structuring the Requirements
Standards, Regulations & Specifications
RCA
OCORA Initiative (OCI)
Other European Initiatives
TOBA
SFERA
EEIG EUG
Shift2Rail1)
Vision & Objective of future CCS (ERA, RUs, IMs)
Functional
Requirements
Non-Functional
Requirements
Interface
Specifications
Functional
Requirements
Non-Functional
Requirements
Interface
Specifications
Functional
Requirements
Non-Functional
Requirements
Interface
Specifications
Program- & Design Requirements
(Design-, Tool-, Process-, Methodology-, Collaboration-, Planning-Requirements, etc.)
Usage Scenarios
A
A
A
A
A
Building Block 1
Building Block 2
Building Block n
System Analysis
System Architecture
C
Design/Implementation
D
B
D
D
D
D
D
D
D
D
OCORA Vision & Objectives of future CCS On-Board
CCS On-Board (COB)
B
B
1) CONNECTA, LINX4RAIL, X2RAIL-4, TAURO

## Slide 55: OCORA Requirements Engineering
  Stakeholder Requirements: OCORA has to manage many different requirements, coming from many different stakeholders.
  Program- & Design Requirements: The OCORA program defines tools, processes, methodologies and design rules to be used within the program and to be considered during the system analysis and the system design/architecture work.
  System Requirements: Requirements in regards to the OCORA system are developed in the MBSE System Analysis (RCA & OCORA), taking into account the A- and B-Level Requirements.
  Building Block Requirements: Requirements in regards to the OCORA building blocks are developed in the MBSE System Architecture (logical / physical), taking into account the MBSE System Analysis. The resulting documentation form the OCORA tender templates, together with the applicable program requirements.
Requirement Definitions
A
B
C
D

## Slide 56: Interaction between CENELEC Process and MBSE
CENELEC PROCESS
Polarion
MBSE
Capella
Concept
System Definition
Risk Analysis
System Requirements
Architecture & Apportionment
CENELEC phases CP1-6 as per EN 50126
A
B
B
Design & Implementation
6
D
System Design
Logical Architecture
Physical Architecture
System Need
System Analysis
Program Requirements
Technical Requirements (partial)
OCORA Scope
CCS On-board
RCA Scope
CCS End-2-End
Linx4Rail Scope
System Need
Operational Analysis
Iteration
C
D
RAMSS
System Analysis
MBSE artefacts to be used in the CP5 (Architecture & Apportionment) documentation and for tenders.
MBSE artefacts to be used in the CENELEC P2 (System Definition) documentation.
C
D
Includes selected A-Level Req.

## Slide 57: OCORA in Context of the relevant CENELEC Projects
Train XX on Track YY (SA)
Integrator (e.g. RU)
OCORA
CENELEC
Process
OCORA Artefacts
Train Type XX (GA)
Integrator (e.g. RU)
CCS On-Board (GA)
Integrator (e.g. RU)
OCORA Building Block n
Chronological
Industry Tasks
OCORA Tasks
Integr. Tasks 1
Integr. Tasks 2
Integr. Tasks 3
OCORA Building Block 2
OCORA Building Block 1 e.g. Vehicle Supervisor
CENELEC P1
CENELEC P2
CENELEC P3
CENELEC P4
CENELEC P5

## Slide 58: OCORA CENELEC Process

## Slide 59: Operational Concept

## Slide 60: Operational Concept Overview
Live Cycle of Passenger, Freight, and Construction Trains
Disposal / out of service
Operate and maintain
Entry in service
Upgrades and updates
Refurbishment / modernisation
+/- 40 years overall life-time
Yearly
Cycle
Maintenance
Type of passengers
Cleaning
Special operation
Yearly
Cycle
Yearly
Cycle
Yearly
Cycle
Passenger Train
Yearly
Cycle
Maintenance
Type of payload
Cleaning
Special operation
Seasonal weather effects
Yearly
Cycle
Yearly
Cycle
Yearly
Cycle
Freight Train
Yearly
Cycle
Maintenance
Type of payload
Cleaning
Special operation
Standard Daily Cycle
Yearly
Cycle
Yearly
Cycle
Yearly
Cycle
Construction Train (Yellow Fleet)
Seasonal weather effects
Starting up train
Driving
Halting / Boarding / Alighting*
Drive train to parking field
Standard Daily Cycle
Shutting down train
Drive train to 1st Platform
Starting up engine
Drive engine to wagons
Driving
Halting / Coupling / De-Coupling
Drive engine to parking field
Standard Daily Cycle
Shutting down train
Starting up engine
Drive engine to construction site
Driving within construction site
Halting / Perform Task
Drive engine to parking field
Shutting down train
Seasonal weather effects
*includes also Coupling / De-coupling